## Slide 1
CPEN 315
Computer Organisation
& Architecture
Final Project 2026
16-bit CPU Design · 32-bit MIPS Processor
University of Ghana — School of Engineering Sciences
Examiner: Prof. Robert A. Sowah

## Slide 2
Project Overview
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
PART A — Logisim Evolution
16-bit CPU Design
ALU with 14 arithmetic + 6 relational operations
Register File: Reg A, B, IR, MAR, MBR, Output
Shared internal bus with tri-state buffers
Program Counter: wraps at address 4
Manual simulation of 4 instruction types
PART B — VHDL / GHDL
32-bit MIPS Processor
6 VHDL components with full testbenches
Instruction Memory (ROM, 16 entries)
CPU Control Unit — combinational logic
ALU Control + Register File (8 × 32-bit)
ALU + Data Memory (256 × 32 RAM)
Waveforms captured in GTKWave (.ghw)

## Slide 3
Part A — 16-bit CPU in Logisim Evolution
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
1
ALU supports 14 arithmetic + 6 relational operations via op-code MUX
2
Instruction formats: R-type, I-type, J-type (all 16-bit wide)
3
Shared internal bus — tri-state buffers control data flow between units
4
Registers: Reg A, Reg B, IR (Instruction), MAR (8-bit), MBR, Output Reg
5
Program Counter wraps at address 4 (0000 → 0001 → 0010 → 0011 → 0000)
Instruction Formats (16-bit)
R-type
op
(4)
rs
(3)
rt
(3)
rd
(3)
fn
(3)
I-type
op
(4)
rs
(3)
rt
(3)
Imm
(6)
J-type
op
(4)
Target Address
(12)

## Slide 4
Logisim 16-bit Full Implementation

## Slide 5
ALU Design — project_ao & project_ro
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Op Code | Operation | Notes
0 | ADD | Adder block
1 | AND | Bitwise
2 | OR | Bitwise
3 | XOR | Bitwise
4 | DIV | Quotient output
5 | MOD | Remainder output
6 | MULT | Lower 16 bits
7 | SUB | Subtract (input tied HIGH)
8–9 | SHL A / B | Logical left shift by 2
10–11 | SHR A / B | Logical right shift by 2
12 | NEG A | 2's complement
13 | NEG B | 2's complement
Relational Unit (project_ro)
Uses Logisim's built-in Comparator block.
Outputs one of 6 conditions selected by a 3-bit RUSel MUX:
EQ · NEQ · GT · GTE · LT · LTE
ALU Architecture
14 arithmetic ops via op-code multiplexer
Output driven by final MUX selecting between arithmetic result and relational result

## Slide 6
Control Unit — Combinational Analysis
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Combinational Analysis
Logisim's built-in tool auto-generates minimised Boolean logic from truth tables
Inputs
OPC7–OPC0 (8-bit opcode) + SC2–SC0 (3-bit step counter)
Outputs
C0–C15 — 16 control signals driving datapath components
Instructions handled
LoadA, LoadB, Arithmetic, Store — 4 instruction types
RAM Contents — Simulation Programme
Address | Hex | Meaning
0x0000 | 0x000A | LoadA from address 10
0x0001 | 0x010D | LoadB from address 13
0x0002 | 0x0200 | Arithmetic — ADD
0x0003 | 0x030A | Store to address 10
0x000A | 0x000A | Operand A = 10
0x000D | 0x000F | Operand B = 15

## Slide 7
Control Unit Implementation

## Slide 8
Part B — 32-bit MIPS Processor in VHDL
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Instruction Memory
ROM, 16 entries
Fully combinational
PC → instruction(32)
CPU Control Unit
opcode(3) → 9 control signals
Combinational logic
Reset drives all to 0
ALU Control Unit
ALUOp(2) + Funct(4)
→ alu_control(3)
Decodes R-type funct field
Register File
8 registers × 32-bit
R0 always reads 0
Sync write, async read
ALU
5 ops: ADD/SUB/AND/OR/SLT
zero flag output
a(32), b(32) → result(32)
Data Memory
256 × 32 RAM
Sync write, async read
addr(32), write_data(32)
Toolchain: GHDL (--std=08) → .ghw waveform file → GTKWave viewer

## Slide 9
Instruction Set Architecture
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Instruction Formats
R-format
op
(3)
rs
(3)
rt
(3)
rd
(3)
funct
(4)
I-format
op
(3)
rs
(3)
rt
(3)
Addr/Imm
(7)
J-format
op
(3)
Target Address
(13)
Instruction | Type | Operation
add | R | R[rd] = R[rs] + R[rt]
sub | R | R[rd] = R[rs] − R[rt]
and / or | R | Bitwise operations
slt | R | Set if less than
lw / sw | I | Load / Store word
beq | I | Branch if equal
addi / slti | I | Immediate arithmetic
j / jal | J | Jump / Jump-and-link

## Slide 10
CPU Control Unit — Signal Mapping
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Instruction | RegDst | ALUSrc | MemtoReg | RegWrite | MemRead | MemWrite | Branch | ALUOp | Jump
R-type | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 10 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 11 | 0
sw | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 11 | 0
addi | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 11 | 0
beq | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 01 | 0
j | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 00 | 1
slti | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 10 | 0
Green = signal asserted (1). ALUOp: 00=pass-through 01=subtract 10=R-type 11=add (for lw/sw/addi)

## Slide 11
VHDL Component Specifications
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Component | Key Ports | Behaviour
Data Memory | clk, addr(32), write_data(32), read_data(32) | Synchronous write, asynchronous read — 256 × 32 RAM
ALU | a(32), b(32), alu_control(3), result(32), zero | 5 operations: ADD / SUB / AND / OR / SLT
ALU Control | ALUOp(2), Funct(4) → alu_control(3) | Decodes funct field for R-type instructions
Register File | clk, rst, 8 registers × 32-bit, R0 always 0 | Synchronous write, asynchronous read
Instruction Memory | pc(32) → instruction(32) | ROM — 16 entries, fully combinational
Control Unit | opcode(3) → 9 control signals | Combinational; reset drives all outputs to 0

## Slide 12
GHDL-Specific Implementation Notes
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Multiplication Width
32×32 = 64-bit result. Always capture in an intermediate variable before slicing to avoid bound-check failures at elaboration time.
No Inline Slicing
(a * b)(15 downto 0) is invalid VHDL-2008 in GHDL. Assign the product to a variable first, then slice it separately.
No Duplicate Signal Drivers
Assigning to the same signal twice in concurrent code causes an elaboration error. Use a single conditional assignment instead.
Simulation Termination
Use std.env.stop at the end of stimulus. Without it, a lone clock process runs forever and hangs GHDL indefinitely.
Procedure Parameters
Never use the signal keyword in procedure parameters when the procedure is called from inside a process — use variable or in/out mode instead.

## Slide 13
Testbench Results — Expected Values
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
Component | Test Case | Expected Output | Pass
Data Memory | Write 1024 → address 2 | Read back 0x00000400 | ✓
Data Memory | Write 429496 → address 4 | Read back 0x00068DF8 | ✓
ALU | ADD 2500 + 25000 | 0x00006B6C (27500) | ✓
ALU | SUB 540250 − 37800 | 0x00076AA2 (502450) | ✓
ALU | AND 53957 & 30000 | 0x00005180 | ✓
ALU | SLT 58847537 < 72464383 | 0x00000001 (true) | ✓
Register File | Write R1 = 1934858 | Read R1 = 0x001D874A | ✓
Register File | Write R0 (zero register) | Always reads 0x00000000 | ✓

## Slide 14
Datapath Testbench — GTKWave

## Slide 15
Development & Simulation Workflow
University of Ghana | CPEN 315 — Computer Organisation & Architecture | 2026
1
Write VHDL
Author entity + architecture for each component. Follow VHDL-2008 std.
2
Analyse
ghdl -a --std=08 *.vhdl
Syntax + semantic check. Errors reported per file.
3
Elaborate
ghdl -e --std=08 tb_name
Link design hierarchy and resolve port maps.
4
Simulate
ghdl -r ... --wave=wave.ghw
Run testbench and emit waveform file.
5
GTKWave
Open .ghw file. Add signals, zoom, verify transitions.
⏱ Stop time formula: 100 ns + (N_tests × 10 ns) + margin
Ensures all stimulus completes before GHDL auto-terminates the simulation.

## Slide 16
Conclusion
16-bit CPU — Complete
Successfully designed a full 16-bit CPU in Logisim with ALU, datapath, and combinational control unit.
32-bit MIPS — All 6 Components
Extended all 6 components to 32-bit in VHDL-2008; all simulate cleanly in GHDL with zero errors.
Testbench Validation
All testbenches validate correct behaviour for every specified test case across Data Memory, ALU, and Register File.
Key Insight
GHDL's strict IEEE-2008 compliance requires careful bit-width management and explicit intermediate variables.
University of Ghana — CPEN 315 — 2026